PRODUCT INFORMATION SHEET

DRIVE CLEAR

ORGANIC GROWTH REMOVER

PRODUCT INFORMATION:

Water based soft wash to effectively destroy bacterial spores, algae spores & other organic growths from a wide range of surfaces such as driveways, tarmacadam, patios, tennis courts, sport surfaces, timber walkways, glass houses, brickwork, tiled roofs etc.

_________________________________________________________

ADVANTAGES:

POWERFUL ANTI-		Drive Clear is a concentrated quaternary ammonium compound

MICROBIAL ACTIVITY:	proven to be an effective organic growth treatment by eradicating the 				spores & algae growing on & below the surface.

SAFE ON ALL SURFACES:	Suitable for use on all external hard surfaces

EASY TO USE:		Requires no rinsing, can be used with sprayer equipment, with a 					watering can or through pressure washing equipment. Results can be 				seen within a few days of treatment.

PCS NO: 100206		Passed by the Dept. of Agriculture, Food & Marine in Ireland

SOLUBILITY:			100% soluble in water.

___________________________________________________________

DIRECTIONS FOR USE:

For best results use in dry weather conditions. Dilute 1:5 with water. The diluted liquid should be sprayed or brushed onto the surface at a rate of 5lts of mixture to 9sqm’s of surface & left on indefinitely. Fully dried out, inactive organic growth can be brushed or washed from surface at a later time. Keep away from water sources & plant life. Do not spray into gullies, traps, gutters or anywhere there may be a risk of water contamination. Do not mix with other chemicals

____________________________________________________________

HEALTH AND SAFETY: See Safety Data Sheet.

____________________________________________________________

PACKAGING:

All our plastic drums are high molecular weight; high-density polyethylene designed to bring the product to the customer in perfect conditions.

Size: 5Lt Drums & 20Lt Drums

___________________________________________________________

QUALITY ASSURANCE: This product is manufactured in Ireland to ISO 9001 quality standards & conforms to R.E.A.C.H, CLP & BPR regulations. Shelf life: Not less than 3 years.

Safety Data Sheet

Corresponding to Regulation (EC) No 1907/2006					Page 1 of 7

Date of issue: 01.01.20								SDS Version No. 2

PRODUCT NAME: DRIVE CLEAR

SECTION 1: IDENTIFICATION OF THE SUBSTANCE/MIXTURE AND OF THE COMPANY/UNDERTAKING

1.1. Product identifier

Product Name 			DRIVE CLEAR

Product No. 				OIR 605

Other means of Identification: 	UFI: 1YN1-20YM-600X-1CJS

1.2. Relevant identified uses of the substance or mixture and uses advised against

Identified uses:			Organic Growth Remover – For Professional Use Only

1.3. Details of the supplier of the safety data sheet

Supplier 				Roschem Products Ltd

Windmill Road, Elphin, Co Roscommon, Ireland

Tel: +353 (0)71 9635375 	Fax: +353 (0)71 9635414

Email:info@roschemproducts.com

1.4. Emergency Contact:  		National Poisons Information Centre, Beaumont Hospital, 					Beaumont Road, Dublin 9. Tel:(01)8092566 (8am-10pm)

SECTION 2: HAZARDS IDENTIFICATION

2.1. Classification of the substance or mixture

Classification: 	Regulation (EC) No 1272/2008:	H302, 	H314, H400

Human health:  	Harmful if swallowed. Causes severe skin burns and eye damage

Environment:  	The product contains a substance which is very toxic to aquatic organisms.

2.2. Label elements

Detergent Labelling: 	Contains: ALKYL DIMETHYL BENZYL AMMONIUM CHLORIDE

DANGER		     WARNING      		      WARNING

Hazard 		H302 		Harmful if swallowed

Phrases 		H314 		Causes severe skin burns and eye damage.

H400 		Very toxic to aquatic life

Precautionary 	P405 & 102 	Store locked up. Keep out of the reach of children

Statements		P260	Do not breathe vapours, spray mists

P262	Do not get in eyes, on skin or on clothing

P264	Wash hands thoroughly after handling

P280	Wear protective gloves, clothing, eye & face protection

P301 & 310	IF SWALLOWED: Rinse out mouth immediately with water. 				Immediately call a poison centre or doctor/physician.

P302	IF ON SKIN: Remove contaminated clothing & rinse skin 					thoroughly with soap & water. Obtain medical attention if irritation 				persists

Safety Data Sheet

Corresponding to Regulation (EC) No 1907/2006					Page 2 of 7

Date of issue: 01.01.20								SDS Version No. 2

P304	IF INHALED: Remove immediately from source to fresh air. Obtain 				medical attention if any discomfort continues.

P305 & 310	IF IN EYES: Flush eyes with water, remove contact lenses if 				present & continue rinsing. Immediately call a poison centre or 				doctor/physician.

P501	Dispose of contents/container to in accordance with local 					regulations. Recover, reclaim or recycle, where possible.

SECTION 3: COMPOSITION/INFORMATION ON INGREDIENTS

3.2. Mixtures

ALKYL DIMETHYL BENZYL AMMONIUM CHLORIDE 10-20% CAS-No.: 68424-85-1 EC No.: 270-325-2 REACH registration No: Exempt

Classification (EC 1272/2008) Acute Tox. 4 - H302 Skin Corr. 1B - H314 Eye Dam. 1 - H318 . Aquatic Acute 1 - H400

A Full Text for all Hazard Statements are Displayed in Section 16

SECTION 4: FIRST AID MEASURES

4.1. Description of first aid measures

Inhalation: 	 	Remove immediately from source to fresh air. Obtain medical attention if 			any discomfort continues.

Skin Contact:		Remove contaminated clothing & rinse skin thoroughly with soap & water. 			Obtain medical attention if irritation persists.

Eye Contact: 	Flush eyes with water immediately. Obtain medical attention if irritation 			persists.

Ingestion: 		DO NOT INDUCE VOMITING! Drink a few glasses of water or milk. Get 			medical attention if any discomfort continues

Protection of

first aider:		Avoid ingestion, contact with skin and eyes (see Section 8.)

4.2. Most important symptoms and effects, both acute and delayed

Inhalation: 		Irritating to respiratory system. Prolonged inhalation of high 					concentrations may damage respiratory system.

Ingestion: 		Causes burns. Swallowing concentrated chemical may cause severe 			internal injury. May cause chemical burns in mouth, oesophagus & 				stomach.

Skin contact: 	Corrosive to skin. Will burn skin on contact

Eye contact: 		Risk of serious damage to eyes. Causes burns. Contact with 				concentrated chemical may very rapidly cause severe eye 					damage, possibly loss of sight.

Safety Data Sheet

Corresponding to Regulation (EC) No 1907/2006					Page 3 of 7

Date of issue: 01.01.20								SDS Version No. 2

4.3. Indication of any immediate medical attention and special treatment needed

The severity of the symptoms described will vary depending on the concentration and the length of exposure.

SECTION 5: FIRE FIGHTING MEASURES

5.1 	Suitable Extinguishing Media: 	Water, Foam.

5.2 	Unsuitable: 				N/A

5.3 	Specific Hazards: 			The thermal decomposition products released oxides 						of nitrogen & carbon) should be considered toxic if 						inhaled.

5.4 	Special Equipment for

the protection of Fire Fighters: 	Wear full protective clothing & breathing 	apparatus.

SECTION 6: ACCIDENTAL RELEASE MEASURES

6.1	Personal Precautions: 		Avoid ingestion, contact with skin & eyes (see 							Section 8.)

6.2	Environmental Precautions: 	Do not discharge into drains, water courses. 							Spillages or uncontrolled discharges into water 							courses must be immediately alerted to the							Environmental Agency or other appropriate							regulatory body

6.3	Methods for Cleaning up: 		Small Spills - Flush with water.

Large Spills - Take up with absorbent material, e.g., sand, sawdust, into tightly closed plastic containers.

SECTION 7: HANDLING AND STORAGE

7.1 	Handling

Technical Measures: 		No special measures required.

Safe Handling Advice: 		Avoid ingestion, contact with eyes & skin. Comply with 					instructions for use.

7.2	Storage

Technical Measures: 		No special measures required.

Storage Conditions: 		Store in a cool dry place.

Incompatible Products: 		Acids, Strong Oxidizing Agents.

Packaging: 				Plastic Drums.

Packaging Materials: 		Recommended: Plastic Materials, Polyethylene, 						Polypropylene. Not Suitable - Uncoated Metal Drums.

Safety Data Sheet

Corresponding to Regulation (EC) No 1907/2006					Page 4 of 7

Date of issue: 01.01.20								SDS Version No. 2

SECTION 8: EXPOSURE CONTROLS/PERSONAL PROTECTION

8.1	Engineering Measures: No special measures required.

8.2	Personal Protection Equipment:

Respiratory Protection:	Provide adequate ventilation in areas of confined space.

Hand Protection:		Use Chemical Resistant Gloves to EN Standard 374 Level 1, 					Letter Code K. Thickness of glove material: 0.7mm. 						Breakthrough time (maximum wear duration) >480 mins

Eye Protection:		Use Chemical Goggles or Face Shield to EN Standard 166 					Level 3 or higher

Skin Protection: 		Wear Plastic Apron EN Standard 13034 Type PB[6] & Face 					Shield EN Standard 166 Level 3 or higher

8.3	Hygiene Measures:		Handle in accordance with good industrial hygiene and

safety practices.

8.4	Occupational Exposure Limits:	N/A

SECTION 9: PHYSICAL AND CHEMICAL PROPERTIES

9.1. Information on basic physical and chemical properties

- Physical state: 					liquid

- Odour / Odour threshold:  				chemical

- Colour:						Pink

- pH:   							6.9

- Melting point / freezing point:			N/A

- Initial boiling point & boiling range:		N/A

- Flash point:						N/A

- Evaporation rate:					N/A

- Flammability solid, gas):				N/A

- Upper/lower flammability or explosive limits:	N/A

- Vapour pressure:					N/A

- Vapour density:					N/A

- Relative density:					0.995kg/dm3

- Solubility(ies):					N/A

- Partition coefficient: n-octanol/water:		N/A

- Particle characteristics:				N/A

- Auto-ignition temperature:				N/A

- Decomposition temperature:			N/A

- Viscosity:						N/A

- Explosive properties:				N/A

- Oxidising properties:				N/A

Safety Data Sheet

Corresponding to Regulation (EC) No 1907/2006					Page 5 of 7

Date of issue: 01.01.20								SDS Version No. 2

9.2.1 Additional information

Physical Hazard Class                                   	N/A

Properties                                                      	N/A

Safety Characteristics                                    	N/A

9.2.2 Other Safety Characteristics

Mechanical Sensitivity                                    	N/A

Acid/Alkaline Reserve                                    	N/A

Conductivity/Redox Potential                         	N/A

SECTION 10: STABILITY AND REACTIVITY

10.1. Reactivity: 					There are no known reactivity hazards 								associated with this product.

10.2. Chemical stability: 				Stable under normal temperature conditions 							and recommended use.

10.3. Possibility of hazardous reactions: 		Hazardous Polymerisation N/A

10.4. Conditions to avoid: 				Avoid Extreme Temperatures. Avoid contact 							with acids &/or oxidising agents.

10.5. Incompatible materials: 			Acids &/or oxidizing agents

10.6. Hazardous decomposition products: 	None under normal conditions.

SECTION 11: TOXICOLOGICAL INFORMATION

11.1 Information on Hazard Classes as defined in regulation (EC) No 1272/200               	N/A

11.2 Information on other Hazard Classes which related to endocrine disrupting properties as determined by the aforementioned regulations.                                 	          			 N/A

11.3. Information on toxicological effects:

Inhalation: 		Irritating to respiratory system. Prolonged inhalation of high 					concentrations may damage respiratory system.

Ingestion: 		Swallowing concentrated chemical may cause severe 	internal injury. May 			cause chemical burns in mouth, oesophagus & stomach.

Skin contact: 	Corrosive to skin. Will burn skin on contact

Eye contact: 		Risk of serious damage to eyes. Causes burns. Contact with 				concentrated chemical may very rapidly cause severe eye damage, 			possibly loss of sight.

11.4. Toxicological information on ingredients:

ALKYL DIMETHYL BENZYL AMMONIUM CHLORIDE CAS-No.: (68424-85-1)

Acute toxicity:

Acute Toxicity (Oral LD50)

150 mg/kg Mouse

Acute Toxicity (Dermal LD50)

1420 mg/kg Rat

Miscellaneous information sources.

Safety Data Sheet

Corresponding to Regulation (EC) No 1907/2006					Page 6 of 7

Date of issue: 01.01.20								SDS Version No. 2

SECTION 12: ECOLOGICAL INFORMATION

Eco-toxicity

This product is Readily Biodegradable and not expected to be hazardous to the environment.

12.1. Toxicity

Ecological information on ingredients:

ALKYL DIMETHYL BENZYL AMMONIUM CHLORIDE CAS-No.: (68424-85-1)

Acute Toxicity - Fish

LC50 96 hours 0.31 mg/l Lepomis macrochirus (Bluegill)

Miscellaneous information sources.

12.2. Persistence and degradability

Degradability: The surfactant(s) contained in this preparation comply with the biodegradability criteria as laid down in Regulation (EC) No.648/2004 on detergents. Data to support this assertion are held at the disposal of the competent authorities of the Member States and will be made available to them, at their direct request or at the request of a detergent manufacturer.

12.3. Bioaccumulative potential			No data available on bioaccumulation.

12.4. Mobility in soil					Mobility: The product is soluble in water.

12.5. Results of PBT and vPvB assessment	Not determined.

12.6. Other adverse effects			Not determined.

SECTION 13: DISPOSAL CONSIDERATIONS

General information: Waste to be treated as controlled waste. Disposal to licensed waste disposal site in accordance with local Waste Disposal Authority

13.1. Waste treatment methods

Dispose of waste in accordance with local regulations. Recover, reclaim or recycle, where possible.

SECTION 14: TRANSPORT INFORMATION

REGULATIONS			CLASS

RID/ADR:				8/III

ICAO/IATA-DGR:			8 /1760/III

GGVSee/IMDG-Code:		8/1760/III

14.1. UN number				UN 1760

14.2. UN proper shipping name

CORROSIVE LIQUID, N.O.S. (ALKYL DIMETHYL BENZYL AMMONIUM CHLORIDE)

Safety Data Sheet

Corresponding to Regulation (EC) No 1907/2006					Page 7 of 7

Date of issue: 01.01.20								SDS Version No. 2

14.3. Transport hazard class(es)		Class 8 Corrosive

14.4. Packing Group			III

14.5. Environmental Hazards

Environmentally Hazardous Substance/Marine Pollutant: N/A

14.6. Special precautions for user		NA

14.7. Transport in bulk according to Annex II of MARPOL73/78 and the IBC Code 	N/A

SECTION 15: REGULATORY INFORMATION

15.1. Safety, health and environmental regulations/legislation specific for the substance or mixture

EU Legislation

Regulation (EC) No 1907/2006 - Registration, Evaluation, Authorisation and Restriction of Chemicals (REACH) (as amended)

Regulation (EC) No 1272/2008 of the European Parliament & of the Council of 16 December 2008 on classification, labelling & packaging of substances & mixtures (as amended)

Regulation (EC) No 648/2004 of the European Parliament & of the Council of 31 March 2004 on detergents (as amended)

Commission Regulation (EU) 2020/878 of 18 June 2020

15.2. Chemical Safety Assessment

No chemical safety assessment has been carried out.

SECTION 16:	OTHER INFORMATION

Revision Comments

Re-issued according to Regulation (EU) No 2020/878

Revision Date: 		01.09.21

Revision No: 			2

Replaces version of: 	01.01.20

Hazard Statements In Full

H302 	Harmful if swallowed.

H314 	Causes severe skin burns and eye damage.

H318	Causes serious eye damage

H400 	Very toxic to aquatic life

The information contained herein is based on the present state of our knowledge and is intended to describe our products from the point of view of safety requirements. It should therefore not be construed as guaranteeing specific properties.